| LHC-LQN-ES-0001.00 rev.2.0 AT-CRI-SSA/Smi 383921 2005-02-23 |
| --- |
| Engineering Specification |
| SHORT STRAIGHT SECTION TYPES IN THE DISPERSION SUPPRESSORS |
| Abstract This Engineering Specification defines equipment codes in the LHC Dispersion Suppressors for the Cold Mass (CM) mechanical assemblies, cryostats and Short Straight Section (SSS DS) types from Q11 to Q8. A total of 20 different types of CM mechanical assemblies, 16 cryostat types and 34 different SSS types are identified. |
| Prepared by: Martin Schmidlkofer LHC-CRI Martin.Schmidlkofer@cern.ch | To be Checked by: Samy Chemli Vittorio Parma Herve Prin Karl-Martin Schirm Nicolaas Kos | To be Approved by: Michele Modena |
| LHC Short Straight Sections List: A. Ballarino, Ch. Boccard, P. Bonnal, D. Bozzini, J. Casas-Cubillos, P. Cruikshank, L. Evans, D. Hagedorn, C. Hauviller, A. Ijspeert, K. Kershaw, Ph. Lebrun, M. Mayoud, R. Ostojic, V. Parma, A. Poncet, H. Prin, P. Proudlock, J-P. Quesnel, G. Riddone, L. Rossi, I. Ruehl, R. Saban, K-M. Schirm, H. Schmickler, M. Schmidlkofer, R. Schmidt, G. Schneider, A. Siemko, P. Strubin, L. Tavian, J-Ph. Tock, Th. Tortschnanoff, G. Trinquart, M. Vitasse, R. van Weelderen, L.R. Williams |
| History of Changes |
| Rev. No. | Date | Pages | Description of Changes |
| 0.1 – draft 0.2 – draft 1.0 2.0 | 2003-05-05 2003-05-09 2003-06-20 2005-02-23 | All All All | Version 0.1-draft prepared by Lars Nielsen. Version 0.2-draft checked by V. Parma, H. Prin, K-M. Schirm and sent for approval to the LHC Short Straight Section list. Deadline: 23 May 2003. In total 3 new cryostat types added (QQDOS, QQDPS and QQDQS) taking into account the difference of the IFS connection tube depending on the IFS type (see tables 2, 3, 4). Version 1.0 released. Update to optics version 6.5 (no changes). In total 4 new SSS types added (QQNCE, QQNJF, QQNJG and QQNJI) taking into account the difference beam screen types. |

Table of Contents

1.	introduction	4

2.	EQUIPMENT CODE NAMES	4

2.1	EQUIPMENT CODES FOR CM ASSEMBLIES	4

2.2	EQUIPMENT CODES FOR CRYOSTATS	6

2.3	EQUIPMENT CODES FOR SHORT STRAIGHT SECTIONS	7

3.	SSS DS, CRYOSTAT AND COLD MASS LOCATIONS	8

4.	reference	8

# introduction

This Engineering Specification defines the equipment codes of the Cold Mass (CM) mechanical assemblies, cryostats and SSS types in the LHC Dispersion Suppressors, Q11 to Q8.

The magnet configuration in the present Engineering Specification is based on LHC optics version 6.5. The cryogenic parameters are based on the Engineering Specification 
LHC-Q-ES-0001 [1], which specifies all cryogenic parameters including phase separators and QQS types.

The electric power scheme is defined by the Engineering Specification LHC-DCC-ES-0003 [2], which, together with the diode layout and naming given by CEA, defines the scheme for the bus-bar plugs.

# EQUIPMENT CODE NAMES

## EQUIPMENT CODES FOR CM ASSEMBLIES

The general equipment codes for the SSS DS Cold Mass (CM) assemblies are:

LMQM_	Cold mass assembly for quadrupole magnet MQM_

LMQT_	Cold mass assembly for quadrupole magnet MQ and MQT.

In total 20 different types of SSS DS cold mass assemblies are identified; their equipment codes are listed in Table 1. In addition to the different types of MQ quadrupole and corrector magnets, the assigned cold mass equipment codes also takes into account the different assembly types given by the diode type and the front cover.

A diode in installed at cold masses of type MQ, depending of the electrical power scheme I can be of the types, according to the naming given by CEA:

A:	Type (FA, DB)

B:	Type (FB, DA).

The front cover type, depending on the QQS type, is specified as:

A:	Front cover with one quench/cool-down and warm-up pipe connector.

B:	Front cover with pressure restriction plug and two quench/cool-down and warm-up pipe connectors.

Z:	Front cover without quench/cool-down and warm-up pipe connectors.

The cold mass of all Q11 magnets contains a welding flange for installation of an insulation vacuum barrier, which is shown in Table 1, although this does not cause additional cold mass types.

Table 1 - Cold Mass equipment codes

| Equipment Code | Quantity | Quadrupole mq | Corrector | Diode type | Vacuum Barrier | fRONT cOVER |
| --- | --- | --- | --- | --- | --- | --- |
| LMQMC | 3 | MQML | (F/D) | MCBCA | None | No | Z |
| LMQMD | 19 | MQML | (D/F) | MCBCB | None | No | Z |
| LMQMO | 1 | MQML | (F/D) | MCBCA | None | No | A |
| LMQMP | 1 | MQML | (D/F) | MCBCB | None | No | A |
| LMQMH | 9 | MQMC+MQM | (F/D) | MCBCA | None | No | A |
| LMQMI | 1 | MQMC+MQM | (D/F) | MCBCB | None | No | A |
| LMQMQ | 1 | MQMC+MQM | (F/D) | MCBCA | None | No | Z |
| LMQMR | 1 | MQMC+MQM | (D/F) | MCBCB | None | No | Z |
| LMQTA | 2 | MQ+MQTL | (F/D) | MCBCC | A | No | Z |
| LMQTM | 2 | MQ+MQTL | (F/D) | MCBCC | B | No | Z |
| LMQTB | 2 | MQ+MQTL | (D/F) | MCBCD | A | No | Z |
| LMQTN | 2 | MQ+MQTL | (D/F) | MCBCD | B | No | Z |
| LMQTC | 6 | MQ+MQTL | (F/D) | MSCBA | A | Yes | B |
| LMQTK | 6 | MQ+MQTL | (F/D) | MSCBA | B | Yes | B |
| LMQTD | 2 | MQ+MQTL | (D/F) | MSCBB | A | Yes | B |
| LMQTL | 2 | MQ+MQTL | (D/F) | MSCBB | B | Yes | B |
| LMQTG | 1 | MQ+MQTL+MQTL | (F/D) | MCBCC | A | No | A |
| LMQTO | 1 | MQ+MQTL+MQTL | (F/D) | MCBCC | B | No | A |
| LMQTH | 1 | MQ+MQTL+MQTL | (D/F) | MCBCD | A | No | A |
| LMQTP | 1 | MQ+MQTL+MQTL | (D/F) | MCBCD | B | No | A |

## EQUIPMENT CODES FOR CRYOSTATS

The general equipment code for SSS DS cryostat assemblies is: QQD_S.

16 different types of SSS DS cryostats are identified; their equipment codes are:

Table 2 - Equipment codes for SSS DS cryostats

| Equipment Code | No. | Vacuum Barrier | Length | Phase separator Type | Jumper | no. of BPM feed-throughs | cryogenic tubing | IFS Type 3) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| QQDAS | 18 | No | 6935 | None | nONE | 2 |  | MQM |
| QQDOS | 8 | No | 6935 | None | nONE | 2 |  | MQ |
| QQDBS | 1 | No | 6935 | N | a | 2 | Special 1) | MQM |
| QQDCS | 8 | Yes | 6935 | N | b | 2 |  | MQ |
| QQDDS | 6 | Yes | 6935 | P | b | 2 |  | MQ |
| QQDES | 2 | Yes | 6935 | P | b(high)2) | 2 |  | MQ |
| QQDFS | 2 | No | 8335 | N | A | 2 |  | MQM |
| QQDPS | 2 | No | 8335 | N | A | 2 |  | MQ |
| QQDGS | 4 | No | 8335 | P | A | 2 |  | MQM |
| QQDQS | 2 | No | 8335 | P | A | 2 |  | MQ |
| QQDHS | 2 | No | 8335 | P | A(high)2) | 2 |  | MQM |
| QQDJS | 1 | No | 8335 | None | none | 2 | Special 1) | MQM |
| QQDKS | 4 | No | 6935 | None | nONE | 4 |  | MQM |
| QQDLS | 2 | No | 8335 | N | A | 4 |  | MQM |
| QQDMS | 1 | No | 6935 | N | a | 2 | Special 1) | MQM |
| QQDns | 1 | No | 8335 | None | none | 2 | Special 1) | MQM |
| Total | 64 |

1)	See drawings no. LHCLSQR_R0030 and LHC LHCLSQR_R0031 [3].

2)	Jumper types A(HIGH) and B(HIGH) are +280 mm higher than the standard jumper types.

3)	IFS connection tube depending on the IFS type MQ-type or MQM-type.

## EQUIPMENT CODES FOR SHORT STRAIGHT SECTIONS

The general equipment codes for the SSS DS types are:

LQN__	SSS DS with quadrupole MQM_.

LQT__	SSS DS with quadrupole MQ + MQTL.

Table 3 - Equipment codes for SSS DS types

| SSS DS equipment code | Cryostat equipment code | Cold Mass equipment code | Beam Screen Line V1 | Beam Screen Line V2 | Total Quantity |
| --- | --- | --- | --- | --- | --- |
| LQNCA | QQDAS | LMQMC | HCVSSB_051 | HCVSSB_052 | 1 |
| LQNCB | QQDAS | LMQMD | HCVSSB_053 | HCVSSB_054 | 8 |
| LQNCC | QQDKS | LMQMC | HCVSSB_053 | HCVSSB_054 | 2 |
| LQNCD | QQDKS | LMQMD | HCVSSB_053 | HCVSSB_054 | 2 |
| LQNCE | QQDAS | LMQMD | HCVSSB_051 | HCVSSB_052 | 9 |
| LQNEA | QQDMS | LMQMO | HCVSSB_051 | HCVSSB_052 | 1 |
| LQNEB | QQDBS | LMQMP | HCVSSB_051 | HCVSSB_052 | 1 |
| LQNJA | QQDFS | LMQMH | HCVSSB_079 | HCVSSB_070 | 1 |
| LQNJB | QQDGS | LMQMH | HCVSSB_079 | HCVSSB_070 | 2 |
| LQNJC | QQDLS | LMQMH | HCVSSB_079 | HCVSSB_070 | 1 |
| LQNJD | QQDLS | LMQMI | HCVSSB_079 | HCVSSB_070 | 1 |
| LQNJE | QQDHS | LMQMH | HCVSSB_079 | HCVSSB_070 | 1 |
| LQNJF | QQDGS | LMQMH | HCVSSB_077 | HCVSSB_078 | 2 |
| LQNJG | QQDFS | LMQMH | HCVSSB_077 | HCVSSB_078 | 1 |
| LQNJI | QQDHS | LMQMH | HCVSSB_077 | HCVSSB_078 | 1 |
| LQNKA | QQDJS | LMQMQ | HCVSSB_077 | HCVSSB_078 | 1 |
| LQNKB | QQDNS | LMQMR | HCVSSB_077 | HCVSSB_078 | 1 |
| LQTBA | QQDOS | LMQTA | HCVSSB_053 | HCVSSB_054 | 2 |
| LQTBB | QQDOS | LMQTB | HCVSSB_051 | HCVSSB_052 | 2 |
| LQTBD | QQDOS | LMQTN | HCVSSB_053 | HCVSSB_054 | 2 |
| LQTCA | QQDCS | LMQTC | HCVSSB_053 | HCVSSB_054 | 2 |
| LQTCB | QQDCS | LMQTL | HCVSSB_053 | HCVSSB_054 | 1 |
| LQTCC | QQDDS | LMQTC | HCVSSB_053 | HCVSSB_054 | 3 |
| LQTCD | QQDES | LMQTC | HCVSSB_053 | HCVSSB_054 | 1 |
| LQTCE | QQDES | LMQTK | HCVSSB_051 | HCVSSB_052 | 1 |
| LQTCG | QQDDS | LMQTK | HCVSSB_051 | HCVSSB_052 | 2 |
| LQTCH | QQDCS | LMQTK | HCVSSB_051 | HCVSSB_052 | 3 |
| LQTCL | QQDCS | LMQTD | HCVSSB_051 | HCVSSB_052 | 2 |
| LQTCM | QQDDS | LMQTL | HCVSSB_053 | HCVSSB_054 | 1 |
| LQTCO | QQDOS | LMQTM | HCVSSB_051 | HCVSSB_052 | 2 |
| LQTEA | QQDQS | LMQTG | HCVSSB_079 | HCVSSB_070 | 1 |
| LQTEB | QQDPS | LMQTH | HCVSSB_077 | HCVSSB_078 | 1 |
| LQTEC | QQDPS | LMQTO | HCVSSB_077 | HCVSSB_078 | 1 |
| LQTED | QQDQS | LMQTP | HCVSSB_079 | HCVSSB_070 | 1 |
| Total | 64 |

Beam Screens are defined in drawings LHCVSSB_0081, 83, 84, 85, 120, 121, 122 and 123 [4].

# SSS DS, CRYOSTAT AND COLD MASS LOCATIONS

Table 4 - SSS DS types and locations

|  |  | LEFT |  |  |  | RIGHT |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | Q11L | Q10L | Q9L | Q8L | LS | Q8R | Q9R | Q10R | Q11R |
| Equipment codes | IR1 |
| CM |  | LMQTC | LMQMD | LMQMH | LMQMD |  |  |  | LMQMD | LMQMH | LMQMD | LMQTK |
| Cryostat |  | QQDES | QQDAS | QQDHS | QQDAS |  |  |  | QQDAS | QQDHS | QQDAS | QQDES |
| SSS DS |  | LQTCD | LQNCB | LQNJE | LQNCB |  |  |  | LQNCE | LQNJI | LQNCE | LQTCE |
|  |  | IR2 |
| CM |  | LMQTK | LMQMD | LMQMH | LMQMD |  |  |  | LMQMD | LMQMH | LMQMD | LMQTC |
| Cryostat |  | QQDDS | QQDAS | QQDGS | QQDAS |  |  |  | QQDAS | QQDGS | QQDAS | QQDDS |
| SSS DS |  | LQTCG | LQNCE | LQNJF | LQNCE |  |  |  | LQNCB | LQNJB | LQNCB | LQTCC |
|  |  | IR3 |
| CM |  | LMQTC | LMQTN | LMQTG | LMQTN |  |  |  | LMQTA | LMQTP | LMQTA | LMQTL |
| Cryostat |  | QQDDS | QQDOS | QQDQS | QQDOS |  |  |  | QQDOS | QQDQS | QQDOS | QQDDS |
| SSS DS |  | LQTCC | LQTBD | LQTEA | LQTBD |  |  |  | LQTBA | LQTED | LQTBA | LQTCM |
|  |  | IR4 |
| CM |  | LMQTL | LMQMC | LMQMI | LMQMC |  |  |  | LMQMD | LMQMH | LMQMD | LMQTC |
| Cryostat |  | QQDCS | QQDKS | QQDLS | QQDKS |  |  |  | QQDKS | QQDLS | QQDKS | QQDCS |
| SSS DS |  | LQTCB | LQNCC | LQNJD | LQNCC |  |  |  | LQNCD | LQNJC | LQNCD | LQTCA |
|  |  | IR5 |
| CM |  | LMQTC | LMQMD | LMQMH | LMQMD |  |  |  | LMQMD | LMQMH | LMQMD | LMQTK |
| Cryostat |  | QQDCS | QQDAS | QQDFS | QQDAS |  |  |  | QQDAS | QQDFS | QQDAS | QQDCS |
| SSS DS |  | LQTCA | LQNCB | LQNJA | LQNCB |  |  |  | LQNCE | LQNJG | LQNCE | LQTCH |
|  |  | IR6 |
| CM |  | LMQTK | LMQMP | LMQMQ | LMQMD |  |  |  | LMQMC | LMQMR | LMQMO | LMQTD |
| Cryostat |  | QQDCS | QQDBS | QQDJS | QQDAS |  |  |  | QQDAS | QQDNS | QQDMS | QQDCS |
| SSS DS |  | LQTCH | LQNEB | LQNKA | LQNCE |  |  |  | LQNCA | LQNKB | LQNEA | LQTCL |
|  |  | IR7 |
| CM |  | LMQTD | LMQTM | LMQTH | LMQTM |  |  |  | LMQTB | LMQTO | LMQTB | LMQTK |
| Cryostat |  | QQDCS | QQDOS | QQDPS | QQDOS |  |  |  | QQDOS | QQDPS | QQDOS | QQDCS |
| SSS DS |  | LQTCL | LQTCO | LQTEB | LQTCO |  |  |  | LQTBB | LQTEC | LQTBB | LQTCH |
|  |  | IR8 |
| CM |  | LMQTK | LMQMD | LMQMH | LMQMD |  |  |  | LMQMD | LMQMH | LMQMD | LMQTC |
| Cryostat |  | QQDDS | QQDAS | QQDGS | QQDAS |  |  |  | QQDAS | QQDGS | QQDAS | QQDDS |
| SSS DS |  | LQTCG | LQNCE | LQNJF | LQNCE |  |  |  | LQNCB | LQNJB | LQNCB | LQTCC |

# reference

[1]	Dimensions, Pressures, Temperatures and Sizing of Valves and Piping in the LHC machine Cryostat and Cryogenic Distribution Line, LHC-Q-ES-0001, G. Riddone.

[2]	Powering Layout of the SSS Correction Scheme, LHC-DCC-ES-0003, P. Burla.

[3]	Drawings LHCLQMAP0002, LHCLSQR_R0030, LHCLSQR_R0031.

[4]	Drawings LHCVSSB_0081, LHCVSSB_0083, LHCVSSB_0084, LHCVSSB_0085, LHCVSSB_0120, LHCVSSB_0121, LHCVSSB_0122 and LHCVSSB_0123